## Slide 1
AI-Based Three-Phase Voltage Unbalance Detection
Severity classification for R, Y and B phase voltages
Internship Capstone Project
Python • Machine Learning • Electrical Measurements
Demonstration uses synthetic data; not a protection relay.

## Slide 2
Problem Statement & Objectives
Detect unbalance from three-phase RMS voltage readings.
Calculate average voltage and a documented unbalance metric.
Classify Balanced, Mildly Unbalanced and Severely Unbalanced.
Compare two classifiers and demonstrate unseen readings.
Show new-reading predictions in a Streamlit dashboard.

## Slide 3
Proposed System Architecture
1. Input: Vr, Vy, Vb voltage readings
2. Data cleaning and validation
3. Feature engineering: average voltage and VU%
4. Train Decision Tree and Random Forest
5. Evaluate metrics and save best model
6. Streamlit dashboard for new readings

## Slide 4
Electrical Formula & Labels
Vavg = (VR + VY + VB) / 3
VU% = max(|VR−Vavg|, |VY−Vavg|, |VB−Vavg|) / |Vavg| × 100
Balanced: VU ≤ 1.0%
Mild: 1.0% < VU ≤ 2.0%
Severe: VU > 2.0%
Thresholds are illustrative and must be confirmed for real applications.

## Slide 5
Dataset & Machine Learning
Training dataset: 2,400 synthetic rows.
Separate unseen demonstration dataset: 300 synthetic rows.
80/20 stratified train/test split.
Models: Decision Tree and Random Forest.
Metrics: accuracy, weighted precision, recall, F1-score, confusion matrix.
Run train_model.py to generate the actual measured metrics.

## Slide 6
Dashboard Demonstration
Enter R, Y and B phase voltages.
View average voltage and unbalance percentage.
Compare AI prediction with threshold reference.
Open the unseen-data tab to test separate readings.
Example inputs: 230, 230, 230 V; then 230, 225, 218 V.

## Slide 7
Limitations, Safety & Future Work
Data are synthetic; results do not establish field accuracy.
Confirm the correct unbalance definition and thresholds with the applicable standard.
Use rated isolated sensing equipment and qualified supervision.
Never connect a PC or Arduino directly to mains voltage.
Future: real labelled data, sequence components, trend monitoring and validated alarms.

## Slide 8
Conclusion
End-to-end prototype demonstrates data processing, engineering features, ML classification and visualization.
Useful as an internship learning/demo project.
Field deployment requires real measurements, validation and electrical safety review.
Thank you • Questions?